Cummins Programming

1. get ESN

2. look up ESN on https://parts.cummins.com/

3. type in ESN at top

4. click on option view on left hand side of window
IF ISX or ISB or any other IS? You MUST GET ECM CODE

ISX ECM CODE IS IN product information section

5. in the filter by Option Number/Name area you will search for SC
- SC – write down SC number
  - if it is blue click on it and write down CPL if available

6. in the filter by Option Number/Name area you will search for DO
DO – write down DO number

7. in the filter by Option Number/Name area you will search for module
- Module - look for engine control module partnumber
- click all blue options until you get a diagram with ECM on it

ECM diagram example:

8. open cummins insite and connect to ECM

connect to ecm button

9. click calibration selection

select engine type and ECM partnumber

select calibration according to SC, CPL, DO and Horsepower using drop downs or IF ISX USE THE ECM CODE
  - if SC does not give you correct programming for the horsepower customer request
  - use CPL to filter out engines
    - CPL must match the one for engine if necessary use SC number to see what CPL is selected then keep filtering without the SC
  - then use Horsepower
    - use max governed speed

once you have filtered out calibrations send to ecm by right clicking on it and selecting transfer to ecm
  - only calibrations with green check mark are available so when multiple are left only the green one can be sent