Caterpillar Fixing Steps

SECTION 1
no comm

1. Does it have Powers?
If no then ohm all transistors on edges

2. Does it comm ?
If no then do intel and small x25160 or at25640N

3. Still no Comm after doing chips intel and small x25160 or at25640n?
 then change RAMs

4. Still no comm
then do inj chips under plug

5. Still no comm
then ohm transistors on edges again

6. still no comm
put notes on tag and move onto next one most likely if good power but no comm it will be CPU

SECTION 2
no injectors

1. are all injectors not working?
Change return transistors

2. still no injectors on all ?
Change injector chips under plug

3. only some injectors not working ?
Ohm all injector transistors on edge look at picture

4. all injector transistors ok no shorts
then ohm all diodes next to the injector transistors

5. all diodes ok ?
Then check tiny little 3 leg transistors near plug that are also injector related

6. still no power on some injectors but not all
then ohm all parts on the injector circuit and compare with injectors that are working